8W 2.4Ghz Wifi Wireless Broadband Amplifier Router Power Range Signal Booster

Model：EP-AB003

Product Description:

Power Amplifier: YP242034

Switch: AS193+FMS2031

1.Brand new and high quality. 
2. Low-noise receive gain. 
3. Signal activity LED indicates 
4. High Gain, High Value, High Performance. 
5. Maximum output power of 8000mW by the Booster. 
6. Plug-and-play, Easy installation, no driver needed. 
7. Ideal for increase the 2400-2500 MHz frequency devices. 
8. Increase the effective range and coverage area of your Wi-Fi network. 
9. Simply attach the booster in between the standard antenna on a wireless router or wireless access point and watch your range grow. 
10. The amplified wireless signal may even penetrate complex environments with many walls and obstacles. 
11. Ideal for use with 2.4GHz Wireless LANs, Support 802.11b, 802.11g, 802.11n (2.4Ghz mode only).

Using Precautions
1.Recommend the input power of RFIN port to between 7dBm and 13dBm.
2.Make sure all power supply to the booster and the AP/Router unit be disconnected before removing or changing antenna.
3.When finishing connecting the booster and the AP/Router, restore power supply first to the booster and then to AP/Router subsequently.
4Waterproof, lightning protection equipment should be attached to outdoor antenna.
5. Keep away from heat and keep ventilated.
6. Please comply with local regulations of electromagnetic radiation.

NOTE: The item need connect with the Access Point Router together, then it can work and the Access Point Router is NOT included.

Specifications:

1. Operation Range: 2400-2500 MHz.

2. Operation Mode: Bi-directional, half-duplex, Auto-Switching via carrier sensing.

3. Frequency Response: ± 1dB over operation range.

4. Input Power: 3dBm (Min.)-20dBm (Max.).

5. Input Power 5 ~ 20 dBm.

6. Optimal Input Power 9 ~ 13 dBm.

7. Output Power: 8000mW/39dBm nominal for 802.11b/11Mbps.

8. Connector: SMA Receptacle, 50 ohm.

9. Transmit Gain: 17dBm nominal.

10. Receiver Gain: 11dBm.

11. Receive Noise Figure: 3.0dBm nominal.

12. Operating Temperature: -40 to 70 degree.

13. Operating Humidity: Up to 95% relative humidity.

14. Material: Cast Aluminum.

15. Size:10.3cm x 7.7cm x 2.1cm

16. Weight: 785g

Package Included:

1 x Booster

1 x Power plug

1 x SMA Cable

1 x 6Dbi antenna